ACN 000 145 193

WARRUGANG SKI CLUB LIMITED

# LODGE OPENING & CLOSING PROCEDURES – SUMMER

## OPENING PROCEDURES

1. LIGHT & POWER     (Main switch board located outside Ski Entrance door).

a)    Main Switch MUST be left on at all times as it runs Exit Lights & Fire Alarm.

b)    Turn on 3 sub main switched  – Ground Floor - Basement - First Floor

2. FIRE ALARM    Do NOT touch Fire Alarm Board in ski entrance foyer under any circumstance. If

in doubt  consult with Perisher Valley Fire Station.

3. WATER     Main’s tap MUST be left on at all times.

4. GAS     (3 gas bottles at Northern end of building beside garage)

a)    MAKE SURE YELLOW GAS COCK IS IN THE OFF POSITION (REF. 5C) AND ALL GAS

JETS ON THE KITCHEN COOK TOP, OVEN AND GRIDDLE PLATE ARE TURNED OFF.

- All three bottles run in one line. Turn all three on (screw valves are under each

individual lid).

- To operate Cook Top, Oven, and Griddle turn on yellow gas cock on right hand side of cooker at floor level so arm is parallel to gas line.

5. HOT WATER     The gas fired Hot Water system is started up by turning on the HW switch located on the wall in the stairwell near the summer entrance door. If in doubt contact one of the emergency

contacts listed on this handout.

- Once the HWS switch  has been switched on the heater will start to heat

water. This will take a period of time so please be patient. The HWS is gas fired so ensure gas is turned on first (step 4 above)

6. COOK TOP     Cook Top is ready for use when gas bottles and yellow gas cock are turned on.

7. OVEN

a)    Turn oven knob at right hand side of control panel to pilot position (spark symbol *).

b)    Push in and hold.

c)    Simultaneously push red ignition button until pilot light ignites (look through round spy hole at

the base of the oven).

d)    Once lit, keep holding oven knob in for approximately 30 seconds.

8. GRIDDLE PLATE

a)    Turn griddle knob anti clockwise to pilot position (spark symbol *) and push down.

b)    Simultaneously push red ignition button until pilot light ignites.

c)    Once lit, keep holding in Griddle knob for approximately 30 seconds.

9. REFRIGERATORS	Close doors and turn on as required.

10. DISHWASHER        	Do NOT use.

11. MICROWAVE	a) Use kitchen microwave only ( instructions are on shelf near microwave).

b) Do NOT use the microwave if you are not conversant  			                  with this type of appliance.

12. HEATING		a) There is adequate firewood for the common room fire (stored in garage).		               b) The central heating system (CHS) can be turned on at the CHS switch

located on the wall in the stairwell near the summer entrance.

### SEE OTHER SIDE FOR LODGE CLOSING PROCEDURE

#### CLOSING PROCEDURES

1. CLEANING UP         a) Remember other guests are using the lodge after you, please

make it easy for them by cleaning up last thing before you leave.

b) REMOVE ALL RUBBISH AND FOOD ETC. There should be large

disposable bins in  the Valley, near the Terminal Buildings area.

2. HEATING	            a) Clean out fireplace and ensure all embers, charcoal etc are completely

dead – if necessary put outside in a metal bucket with water to ensure

no sparks or hot material remains.

b) Ensure wood storage areas on either side of the fireplace are stacked

with wood.

c) Turn off the central heating system

3. STOVE & GAS         a) MAKE SURE COOK TOP, OVEN, & GRIDDLE  PLATE ARE TURNED      	                              TO OFF (push oven and griddle knobs in and turn to 0).

b) Turn off yellow gas cock on right hand side of cooker.

c) Turn all 3 gas cylinders off.

4. REFRIGERATORS  a) Clean out all used refrigerators and defrost.

b) Place wooden chocks in position to prevent doors closing.

c) Turn off at power point.

5. HOT WATER            Turn off the hot water system

6. WATER                      a) Mains tap MUST be left on at all times.

b) Ensure all taps are off and no water is flowing within the lodge

i.e. toilets etc.

7. WINDOWS,                a) Close and secure all windows.

CURTAINS,                b) Close all blinds (bedrooms) and rehang sheets (common room).

DOORS                        c) Close all internal doors and check that all external doors including fire

escape doors are securely closed.

8. LIGHT & POWER     a) Ensure all light switches are turned off.

b) Turn off 3 sub main switches in main switch board – Ground Floor –

Basement – First Floor.

c) LEAVE MAIN SWITCH ON.

9. FINAL CHECK           a) HAVE YOU COMPLETED ALL ITEMS 1 – 8? IF NOT DO SO NOW.

b) ENSURE ALL WINDOWS & DOORS ARE SECURELY LOCKED.

c) ENSURE ALL YOUR RUBBISH IS REMOVED BEFORE YOU GO.

10. FINALLY                  ENSURE YOU PROMPTLY RETURN THE KEY TO THE BOOKING

OFFICER.

EMERGENCY CONTACTS		Peter Funnell		0423 111 392

(02) 9816 2121

Carl Banning		0412 613 948

(02) 9520 7895

David Arens		0414 759 183

### SEE OTHER SIDE FOR LODGE OPENING PROCEDURES

Document revised 27th February 2015